## Slide 1: Network
Introduction to
Computer Networks
Slide Source: Cisco Networking

## Slide 2: Networking Today
Network has no boundary and supports the way we:
  Learn
  Communicate
  Work
  Play

## Slide 3: Providing Resources in a Network
Networks of Many Sizes
  Small Home / Office Networks
  Medium to Large Networks
  World Wide Network
Clients and Servers
  Clients request and display information
  Servers provide information to other devices on the network
Peer-to-Peer
  Computers can be both server and client at the same time.
  What are the advantages?
  What are the disadvantages?

## Slide 4: Network Components
End Devices
  Either the source or destination of a message
  Name some end devices
Intermediary Network Devices
  Connect multiple individual networks to form an internetwork
  Connect the individual end devices to the network
  Ensure data flows across the network
  Provide connectivity
Network Media
  Provide the pathway for data transmission
  Interconnect devices
  Name the three types of media

## Slide 5: Network Components
Network Representations
  What do the symbols represent?
Topology Diagrams
  Physical
  Logical

## Slide 6: LANs and WANs
Local Area Networks
  Spans across small geographical area
  Interconnects end devices
  Administrated by a single organization
  Provide high speed bandwidth to internal devices
WAN Area Networks
  Interconnects LAN
  Administrated by multiple service providers
  Provide slower speed links between LANS
Can you name more network types?

## Slide 7: The Internet, Intranets, and Extranets
The Internet
  Worldwide collection of interconnected networks
  Not owned by any individual or group
Intranets and Extranets

## Slide 8: The Network as a Platform Converged Networks
Traditional Separate Networks
  Each network with its own rules and
The Converging Network
  Capable of delivering data, voice, and video over the same network infrastructure

## Slide 9: What is Communication?

## Slide 10: Establishing the Rules
An identified sender and receiver
Agreed upon method of communicating (face-to-face, telephone, letter, photograph)
Common language and grammar
Speed and timing of delivery
Confirmation or acknowledgment requirements

## Slide 11: Message Encoding

## Slide 12: Message Formatting and Encapsulation
Example: Personal letter contains the following elements:
Identifier of the recipient’s location
Identifier of the sender’s location
Salutation or greeting
Recipient identifier
The message content
Source identifier
End of message indicator

## Slide 13: Message Size
An overview of the segmenting process:
The size restrictions of frames require the source host to break a long message into individual pieces (or segments) that meet both the minimum and maximum size requirements.
Each segment is encapsulated in a separate frame with the address information, and is sent over the network.
At the receiving host, the messages are de-encapsulated and put back together to be processed and interpreted.

## Slide 14: Message Timing
Access Method
Flow Control
Response Timeout

## Slide 15: Network Protocols
How the message is formatted or structured
The process by which networking devices share information about pathways with other networks
How and when error and system messages are passed between devices
The setup and termination of data transfer sessions

## Slide 16: Interaction of Protocols
Application Protocol – Hypertext Transfer Protocol (HTTP)
Transport Protocol – Transmission Control Protocol (TCP)
Internet Protocol – Internet Protocol (IP)
Network Access Protocols – Data link & physical layers

## Slide 17: Protocol Suites and Industry Standards

## Slide 18: Creation of Internet, Development of TCP/IP
The first packet switching network and predecessor to today’s Internet was the Advanced Research Projects Agency Network (ARPANET), which came to life in 1969 by connecting mainframe computers at four locations.
ARPANET was funded by the U.S. Department of Defense for use by universities and research laboratories. Bolt, Beranek and Newman (BBN) was the contractor that did much of the initial development of the ARPANET, including creating the first router known as an Interface Message Processor (IMP).
In 1973, Robert Kahn and Vinton Cerf began work on TCP to develop the next generation of the ARPANET. TCP was designed to replace ARPANET’s current Network Control Program (NCP).
In 1978, TCP was divided into two protocols: TCP and IP. Later, other protocols were added to the TCP/IP suite of protocols including Telnet, FTP, DNS, and many others.

## Slide 19: TCP/IP Protocol Suite and Communication

## Slide 20: Benefits of Using a Layered Model

## Slide 21: The OSI Reference Model

## Slide 22: The TCP/IP Reference Model
Notes: 3.2.4.3 The TCP/IP Protocol Model

## Slide 23: Comparing the OSI and TCP/IP Models

## Slide 24: Communicating the Messages
Segmenting message benefits
  Different conversations can be interleaved
  Increased reliability of network communications
Segmenting message disadvantage
  Increased level of complexity

## Slide 25: Protocol Data Units (PDUs)
Data
Segment
Packet
Frame
Bits

## Slide 26: Protocol Encapsulation

## Slide 27: Protocol De-encapsulation

## Slide 28: Accessing Local Resources
Notes: 3.3.2.1 Network Addresses and Data Link addresses

## Slide 29: Communicating with Device / Same Network

## Slide 30: MAC and IP Addresses
PC1
192.168.1.110
AA-AA-AA-AA-AA-AA
PC2
192.168.1.111
BB-BB-BB-BB-BB-BB
FTP Server
192.168.1.9
CC-CC-CC-CC-CC-CC
R1
192.168.1.1
11-11-11-11-11-11
ARP
Request
S1
R1

## Slide 31: Default Gateway

## Slide 32: Communicating Device / Remote Network

## Slide 33: Introduction to ARP

## Slide 34: ARP Functions/Operation
ARP Table
Used to find the data link layer address that is mapped to the destination IPv4 address.
As a node receives frames from the media, it records the source IP and MAC address as a mapping in the ARP table.
ARP Request
Layer 2 broadcast to all devices on the Ethernet LAN.
The node that matches the IP address in the broadcast will reply.
If no device responds to the ARP request, the packet is dropped because a frame cannot be created.
Note: Static map entries can be entered in an ARP table, but this is rarely done.

## Slide 35: ARP Operation

## Slide 36: Physical Layer Fundamental Principles
Media | Physical Components | Frame Encoding Technique | Signalling Method
Copper Cable | UTP Coaxial Connectors NICs Ports Interfaces | Manchester Encoding Non-Return to Zero (NRZ) techniques 4B/5B codes are used with Multi-Level Transition Level 3 (MLT-3) signaling 8B/10B PAM5 | Changes in the electromagnetic field Intensity of the electromagnetic field Phase of the electromagnetic wave
Fiber Optic Cable | Single-mode Fiber Multimode Fiber Connectors NICs Interfaces Lasers and LEDs Photoreceptors | Pulses of light Wavelength multiplexing using different colors | A pulse equals 1. No pulse is 0.
Wireless Media | Access Points NICs Radio Antennae | DSSS (direct-sequence spread-spectrum) OFDM (orthogonal frequency division multiplexing) | Radio waves

## Slide 37: Copper Cabling Copper Media
Shielded Twisted Pair (STP) Cable
Unshielded Twisted Pair (UTP) Cable
Coaxial Cable

## Slide 38: Copper Cabling UTP Cable

## Slide 39: Copper Cabling STP Cable
Foil Shields
Braided or Foil Shield

## Slide 40: Copper Cabling Coaxial Cable

## Slide 41: UTP Cabling
UTP cable does not use shielding to counter the effects of EMI and RFI. Instead, cable designers have discovered that they can limit the negative effect of crosstalk by:
Cancellation
Varying the number of twists per wire pair

## Slide 42: UTP Cabling UTP Connectors

## Slide 43: UTP Cabling Types of UTP Cable

## Slide 44: Fiber Optic Cabling Properties of Fiber Optic Cabling
Fiber-optic cabling is now being used in four types of industry:
Enterprise Networks
Fiber-to-the-home (FTTH) and Access Networks
Long-Haul Networks
Submarine Networks

## Slide 45: Fiber Optic Cabling Network Fiber Connectors

## Slide 46: Types of Wireless Media
 | IEEE 802.11 standards Commonly referred to as Wi-Fi. Uses CSMA/CA Variations include: 802.11a: 54 Mbps, 5 GHz 802.11b: 11 Mbps, 2.4 GHz 802.11g: 54 Mbps, 2.4 GHz 802.11n: 600 Mbps, 2.4 and 5 GHz 802.11ac: 1 Gbps, 5 GHz 802.11ad: 7 Gbps, 2.4 GHz, 5 GHz, and 60 GHz
 | IEEE 802.15 standard Supports speeds up to 3 Mb/s Provides device pairing over distances from 1 to 100 meters.
 | IEEE 802.16 standard Provides speeds up to 1 Gbps Uses a point-to-multipoint topology to provide wireless broadband access.

## Slide 47: Introduction to the Ethernet Frame
Preamble and Start Frame Delimiter Fields –
Used for synchronization between the sending and receiving devices.
Length/Type Field –
Defines the exact length of the frame's data field; describes which protocol is implemented.
Data and Pad Fields –
Contains the encapsulated data from a higher layer, an IPv4 packet.

## Slide 48: Introduction to the Ethernet Frame (cont.)
Frame Check Sequence Field
Used to detect errors in a frame with cyclic redundancy check (4 bytes); if calculations match at source and receiver, no error occurred.

## Slide 49: End-to-End Connectivity, MAC, and IP (cont.)
Notes: 5.1.4.2 End-to-End Connectivity, MAC, and IP (cont.)

## Slide 50: LAN and WAN Frames
Notes: 4.4.4.5 LAN and WAN Frames

## Slide 51: The Network Layer
The network layer, or OSI Layer 3, provides services to allow end devices to exchange data across the network. To accomplish this end-to-end transport, the network layer uses four basic processes:
Addressing end devices
Encapsulation
Routing
De-encapsulating
Notes: 6.1.1.1 The Network Layer

## Slide 52: Network Layer Protocols
Common network layer protocols include:
IP version 4 (IPv4)
IP version 6 (IPv6)
Legacy network layer protocols include:
Novell Internetwork Packet Exchange (IPX)
AppleTalk
Connectionless Network Service (CLNS/DECNet)
Notes: 6.1.1.2 Network Layer Protocols

## Slide 53
IP Components

## Slide 54: IP - Connectionless

## Slide 55: Best Effort Delivery

## Slide 56: IP – Media Independent

## Slide 57: IPv4 Packet Encapsulating IP

## Slide 58: IPv4 Packet IPv4 Packet Header
Contents of the IPv4 packet header

## Slide 59: IPv4 Packet IPv4 Header Fields
Contents of the IPv4 header fields

## Slide 60: Unicast Address

## Slide 61: Broadcast MAC Address

## Slide 62: Multicast Address
Multicast MAC address is a special value that begins with 01-00-5E in hexadecimal
Range of IPV4 multicast addresses is 224.0.0.0 to 239.255.255.255

## Slide 63: Sample IPv4 Headers in Packet Tracer

## Slide 64: Limitations of IPv4
IP Address depletion
Internet routing table expansion
Lack of end-to-end connectivity
Notes: 6.1.4.1 Limitations of IPv4

## Slide 65: IPv6
Increased address space
Improved packet handling
Eliminates the need for NAT
Integrated security
4 billion IPv4 addresses 4,000,000,000
340 undecillion IPv6 addresses 340,000,000,000,000,000,000,000,000,000,000,000,000

## Slide 66: Encapsulating IPv6

## Slide 67: IPv6 Packet Header
Version | Traffic Class |  | Flow Label |  |  | 
Payload Length |  |  |  | Next Header | Hop Limit | 
Source IP Address |  |  |  |  |  | 
Destination IP Address |  |  |  |  |  | 
Byte 1
Byte 2
Byte 3
Byte 4